## Slide 1: GENESIS IDEATHON
T E A M & D O M A I N
Team Name – Nexora
Team Members :
                1. Kavisri S - CB.EN.U4CCE26131
        2. Kaushik P - CB.EN.U4CCE26130
        3. Shruthi Lakshmi V P - CB.EN.U4CCE26151
        4.Gautham Ashokkumar - CB.EN.U4CCE26120
  Selected Domain – Domain #2
  Problem Statement – AI-Powered Predictive Fault Detection and Zero-Downtime
Maintenance for Electrical Grids

## Slide 2: DOMAIN PROBLEM IN OUR WORDS
T E A M
NEXORA
Explanation of the problem in our domain:
What Exactly Needs to Be Solved?
Current grid safety relies on reactive breakers that only trigger after explosions, short circuits, or outages occur. To stop failures beforehand, lightweight AI must run directly on local edge sensors for instant, low-latency analysis of micro-anomalies like high-frequency arcing and micro-voltage drops. This requires affordable, plug-and-play sensor kits to upgrade legacy substations without replacing multi-million-dollar hardware. Additionally, the system must filter out harmless power surges caused by EV fast-chargers and solar backfeed from genuine equipment degradation.
Why Is It Important Right Now?
Aging power networks are facing unprecedented strain from two-way renewable energy flows, dramatically increasing the risk of grid collapse. Undetected insulation breakdown frequently leads to severe transformer explosions, residential fire hazards, and costly machinery damage from unexpected blackouts. Delivering real-time health scores gives grid operators a 48-hour head start to execute zero-downtime maintenance, safeguarding public safety and ensuring continuous energy delivery.
2

## Slide 3: WHO IS AFFECTED?
TEAM
NEXORA
Stakeholder ecosystem around a continuously monitored power grid
PRIMARY USERS
CORE
Grid / utility operators
Real-time operational decisions
Substation operators
Asset status + alarms
Maintenance &
electrical teams
Inspection / repair planning
SECONDARY
STAKEHOLDERS
Transmission & distribution
Network continuity
Renewable-energy
operators
Variable / bidirectional flow
EV infrastructure &
regulators
New load + grid oversight
GRID ASSET + MONITORING LAYER
RELIABLE • CONTINUOUS • PLANNABLE
POWER
WHO BENEFITS?
Homes Businesses
Hospitals
Utilities
Grid

## Slide 4: CURRENT SITUATION & CONTEXT
TEAM
NEXORA
Today’s grid protection isolates faults; the gap is earlier detection of asset degradation
WHAT HAPPENS TODAY?
REACTIVE PROTECTION
Protective relays/breakers act when measured conditions cross protection thresholds; they are not a predictive degradation layer.
CURRENT APPROACH
Normal
grid / asset
Hidden
degradation
Fault
threshold crossed
Trip
relay + breaker
Outage
damage / isolation
Repair
inspect + restore
V / I
TEMPERATURE
GAP → the system reacts to a developed fault; subtle degradation can remain hidden between inspections.
ARCING / PD
NOISE
DESIRED DIRECTION
Opportunity: sense small changes before fault conditions escalate.
Normal
continuous
Sense
monitoring
Detect
early anomaly
Warn
predictive alert
Plan
maintenance window
Continue
power stays on

## Slide 5: KEY CHALLENGES
T E A M
NEXORA
Main difficulties, bottlenecks, root causes and consequences
Main difficulties and bottlenecks
Slow detection: Standard monitoring polls data every few seconds or minutes. Electrical micro-spikes last less than a millisecond, so they pass unseen.
Erratic power flow: Rooftop solar and EV fast chargers push power in both directions. Legacy grid equipment was designed for one-way flow and can't handle this.
Costly upgrades: Replacing multi-million-dollar substations to make them "smart" is not realistic for most utilities.
Root causes behind them
Reactive hardware: Breakers, fuses and relays act only after a short circuit or arc fault has already happened. They protect against damage but do not prevent it.
Invisible signals: Before a transformer fails, it shows small warning signs: transient voltage spikes, harmonic distortion and slight temperature changes. Threshold-based sensors ignore them.
Consequences of leaving them unsolved
Outages and losses: A sudden transformer failure causes a local blackout and halts industrial production, costing manufacturers millions.
Fire and safety risk: Undetected arcing in overhead lines and oil-filled transformers can cause fires and explosive failures in dense urban areas.
Faster asset wear: Overloaded equipment degrades unnoticed, which leads to emergency replacements at a much higher cost.
Takeaway: Faults warn us through micro-anomalies, but nothing is listening.

## Slide 6: EXISTING SOLUTIONS / APPROACHES
T E A M
NEXORA
What is already being done, and where it falls short
SCADA
What it does: It collects substation data and sends it to central servers.
Limitation: The round trip takes seconds to minutes, so it can't intervene in real time.
Industrial APM (ABB Ability, Siemens
MindSphere)
What it does: These cloud platforms are powerful for asset management.
Limitation: They usually require replacing legacy transformers with expensive proprietary hardware, which locks utilities into one vendor.
Overcurrent relays
What it does: They trip when current crosses a fixed limit.
Limitation: Under heavy EV demand they raise false alarms, and they miss slow multi-variable degradation that never crosses the limit.
The Gap They Leave Open: Existing tools watch for big changes after damage has started. Nothing offers low-cost, sub-millisecond prediction at the edge
that detects micro-anomalies and acts before the breaker trips.

## Slide 7: PROBLEM INSIGHTS & OPPORTUNITY AREAS
T E A M
NEXORA
Resources required to solve the problem
Hardware Requirements
CT/PT clamp sensors: They measure current and voltage waveforms without cutting power, so they can be retrofitted onto existing lines.
Edge module: An ESP32, STM32 or Raspberry Pi Edge AI board mounted at the transformer processes data locally in under a millisecond.
Thermal and humidity probes: They track oil and casing temperature to catch heat-related degradation.
Software Requirements
TinyML models: Autoencoders or CNNs learn what normal looks like and flag deviations on the device, with no cloud delay.
Digital twin dashboard: It simulates grid stress, tracks long-term health scores and alerts maintenance teams to failing equipment.
MQTT / Modbus: These lightweight protocols send alerts and summaries to the dashboard using little bandwidth.
Other resources (Including Human
Resources)
Domain experts: Power systems engineers validate fault signatures and waveform models.
Developers: Embedded C/C++ developers build the edge firmware, and full-stack developers build the dashboard.
Utility pilot: Partnering with local distribution companies (DSOs) gives us real grid noise and baseline data to train and test against.
Pipeline: CT/PT sensors → TinyML on edge → MQTT/Modbus → Twin dashboard

## Slide 8: INITIAL DIRECTION & EXPECTED OUTCOME
T E A M
NEXORA
.
What Is Your Expected Outcome?
Predictive Edge Layer: Clip-on sensors install with zero downtime.
On-Device TinyML: On-chip CNNs detect anomalies in sub-milliseconds without cloud latency.
Pre-Fault Warnings: Real-time MQTT alerts schedule maintenance before outages occur.
Expert Validation: Fault signatures are field-tested and verified with local DSOs.
What your team intends to do:
What you want to improve:
Detection Speed: Edge processing detects sub-millisecond spikes that SCADA and cloud tools miss.
Detection Intelligence: Multi-variable AI catches gradual degradation without false alarms from EV demand.
Affordability & Adoption: Retrofit sensor kits upgrade substations without multi-million-dollar hardware replacements.
Safety & Asset Life: Early detection prevents catastrophic fires, explosive failures, and premature equipment loss.
What successful improvement should you achieve:
Faster, Earlier Detection: Sub-millisecond on-device processing alerts before breakers trip.
Higher Accuracy: 90%+ detection precision prevents false alarms during EV and solar load swings.
Fewer Unplanned Outages: Converts catastrophic blackouts and fires into scheduled maintenance.
Low Cost & Scalability: Non-invasive retrofit kits deliver fleet-wide management at a fraction of hardware replacement costs.

## Slide 9: THANK YOU